## Slide 1: Introduction to uncertainty analysis in spatial environmental modelling
Kasia Sawicka and Gerard Heuvelink
Vienna, 24 April 2017

## Slide 2: Uncertainty propagation overview
Model
parameters
Model
structure
Input ± U
Model (± U)
Model
output
Output ± U
Solution
method
Input
data
Data ± U
Observ.
data

## Slide 3: Environmental data vary in space
E.g. Rainfall
Categories like soil type
Environmental quality indicators like soil pH
Notes: As a part of the QUICS project a new tool for uncertainty propagation analysis is developed as a package in R. The Package focuses, but is not limited to, spatial uncertainty analysis.
It is becasue environmental variables vary in space. Like rainfall, soil type, or other environmental quality indicators, for example soil pH.

## Slide 4: Deriving maps is encumbered with error
E.g. interpolation error or error associated with maps derived from other maps
input map A1
input map A2
input map Am
Output map
Notes: The space variation is often displayed by a mean of maps created using various interpolation techniques, for example kriging from point observations or deriving maps from other maps (like DEM and slope) and thus naturally encumbered with interpolation errors. The patterns of uncertainty in space are important because the impacts of correlated error may differ substantially from those associated with random error.

## Slide 5
Fact of life: maps stored in the GIS database are rarely if ever error-free
Causes: generalisation, digitisation, measurement, classification and interpolation errors
Consequence: errors will propagate through GIS operations and spatial models
Key research question: given the errors in the inputs to the GIS operation, how large are the errors in the output?

## Slide 6: Uncertainty propagation analysis involves three steps:
DEFINITION of a (statistical) uncertainty model for spatial objects and attributes
IDENTIFICATION of the uncertainty model (estimate its parameters)
Perform the actual UNCERTAINTY PROPAGATION ANALYSIS

## Slide 7: 1. DEFINITION of the uncertainty model (concentrate on continuous-numerical attributes)
is our (deterministic) representation of the attribute (i.e. the map as stored in the GIS), is the (stochastic) error about it (typically zero mean, but non-zero variance and spatially correlated)
Error is difference between reality and our representation of reality:

## Slide 8: Statistical model of must include:
Marginal pdf at each location (both its shape and parameters)
Spatial correlation (correlogram or semivariogram)
Temporal correlation (for dynamic variables)
Cross-correlation with other uncertain inputs

## Slide 9: 2. IDENTIFICATION of the uncertainty model
Measurement error from instrument and lab specifications, or by taking replicates (always let laboratories analyse duplicates, without telling them!)
Sampling error using sampling theory from statistics (e.g. standard error of the mean, confidence intervals)
Use of ground truth verification data (e.g. control points)
Interpolation error using geostatistics (kriging)
Errors in transfer functions such as regression: R-square
Classification error using multivariate statistics (e.g. maximum likelihood classification remote sensing imagery)
Expert judgement or Expert elicitation (last resort?)
In practice, this may well be the most difficult step of the entire uncertainty propagation analysis

## Slide 10: Performing the actual UNCERTAINTY PROPAGATION ANALYSIS
Taylor series approximation method
Monte Carlo method

## Slide 11: Monte Carlo method
Introduce by means of an example

## Slide 12: Example: computing slope from DEM for a 2 by 2.5 area in the Austrian Alps

## Slide 13: Slope map computed from the DEM (percent):

## Slide 14
Now let the uncertainty about the elevation be  10 meter

## Slide 15: Realisations of uncertain DEM:

## Slide 16: Corresponding slope maps:

## Slide 17: Histograms capture uncertainty in slope:

## Slide 18: Monte Carlo algorithm:
Repeat N times (N  100):
  Simulate a realisation from the probability distribution of the uncertain inputs using a pseudo-random number generator
  Run the model with these inputs and store the result
Analyse the N model outputs by computing summary statistics such as the mean and standard deviation (the latter is a measure of the output uncertainty)

## Slide 19: Performing the actual UNCERTAINTY PROPAGATION ANALYSIS
Taylor series approximation method
Monte Carlo method
Yields the full output pdf, not only the mean and variance
Works with any model
Easy to implement
Advantages Monte Carlo method:

## Slide 20: Monte Carlo method with spatial inputs
Requires that we simulate from the probability distribution of a spatially distributed variable
Can be done with spatial stochastic simulation: instead of kriging, which produces the most likely value (conditional expectation), we generate a possible reality, by simulating from the probability distribution of the spatial variable, using a pseudo-random number generator
Spatial correlations are taken into account
Most popular technique is sequential Gaussian simulation

## Slide 21
Example 1: a possible ‘reality’
Why is it important to include spatial correlation?
1.0
Correlation
Distance

## Slide 22
Why is it important to include spatial correlation?
Example 2: second reality
1.0
Correlation
Distance

## Slide 23
Why is it important to include spatial correlation?
Example 3: third reality
0
Correlation
Distance

## Slide 24
Why is it important to include spatial correlation?
Example 4: fourth reality
1.0
0.8
Correlation
Distance

## Slide 25: Potential applications
Urban drainage models
Biogeochemical models (here, process-based model LandscapeDNDC
Haas et. al. (2013)
Pollution models (here, Metaldehyde Prediction Model)
Risk map
Notes: Now, probably the most interesting thing for you is that the ‘spup’ package would also have a potential for use in industry. It could be used for models like you’ve seen at earlier presentations, e.g. MiStat presented by Arturo, or wastewater treatment plant models, or other.

## Slide 26: Practical excersise – calculating slope from DEM and assosiated uncertainty propagation
Required:
R >= v.3.3.3
Packages
spup
sp
gstat
GGally
gridExtra
purrr
magrittr
DEM
Slope
Link here to share the data/script etc.
Notes: It could be used for models like you’ve seen at earlier presentations, e.g. MiStat presented by Arturo, or wastewater treatment plant models, or other.

## Slide 27
https://github.com/
ksawicka
‘spup’ repository

## Slide 28: DEFINE and IDENTIFY a (statistical) uncertainty model
Marginal pdf at each location (both its shape and parameters)
Spatial correlation (correlogram or semivariogram)
Cross-correlation with other uncertain inputs
IDENTIFICATION
DEFINITION
is our (deterministic) representation of the variable (i.e. the map as stored in the GIS)
is the (stochastic) error about it (typically zero mean, but non-zero variance and spatially correlated)
Notes: Identify uncertainty model
Measurement error from instrument and lab specifications, or by taking replicates (always let laboratories analyse duplicates, without telling them!)
Sampling error using sampling theory from statistics (e.g. standard error of the mean, confidence intervals)
Use of ground truth verification data (e.g. control points)
Interpolation error using geostatistics (kriging)
Errors in transfer functions such as regression: R-square
Classification error using multivariate statistics (e.g. maximum likelihood classification remote sensing imagery)
Expert judgement or Expert elicitation (last resort?)